Cosella-Dörken Products Inc.

4655 Delta Way, Beamsville, Ontario L0R 1B4

Tel. (905) 563-3255 Fax: (905) 563-5582

| Material Safety Data Sheet |
| --- |
| Issue Date: July 11, 2012 |
| Section I—Product Information |
| Product Name | DELTA(-LVC ADHESIVE |
| Product Type | Liquid adhesive |
| Product Use | Liquid substrate adhesive for self-adhesive membranes |
| Section II—Hazardous Ingredients/Identity Information |
| Hazardous Components (Specific Chemical Identity, Common Name(s)) | OSHA PEL | CAS Number | Other Limits Recommended | % of total weight |
| benzene, 1-chloro-4-(trifluoromethyl) |  | 98-56-6 |  | 5-15 |
| CYCLOHEXANE |  | 110-82-7 |  | 1-5 |
| HEPTANE |  | 142-82-5 |  | 1-5 |
| Hexane |  | 110-54-3 |  | 5-15 |
| HYDROCARBON RESINS |  | NA-Mixture |  | 15-30 |
| LIGHT NAPHTHA |  | 64742-89-8 |  | 1-5 |
| Methyl acetate |  | 79-20-9 |  | 35-55 |
| Mineral Oil |  | 64742-52-5 |  | 5-15 |
| SYNTHETIC POLYMER BLEND |  | NA-Mixture |  | 10-20 |
| Extremely flammable liquid and vapor. Vapor may cause flash fire. Harmful or fatal if swallowed. Harmful if absorbed through the skin. Pulmonary aspiration hazard. After ingestion, may enter lungs and produce damage. High vapor concentrations may cause drowsiness. Can cause eye, skin and respiratory tract irritation. |
| Hazards Identifications |
| Inhalation | Skin contact |
| Eve Hazards | Irritation may be severe, causing burns and leading to permanent eye damage. |
| Skin Hazards | May cause skin irritation and contact dermatitis upon prolonged contact. May be absorbed through skin in harmful amounts. |
| Ingestion Hazards | Can cause gastrointestinal irritation, nausea and vomiting. Aspiration of material into the lungs may cause chemical pneumonitis, which can be fatal. Harmful or fatal if swallowed. |
| Inhalation Hazards | Exposure to vapors may cause respiratory tract irritation. Inhalation of vapors or mists may cause central nervous system depression, light-headedness, headache, nausea and loss of coordination. |
| Subchronic (Target Organ Effects) | Central nervous system. |
| Chronic/Carcinogenicity Effects | Damage to the nervous system of the extremities, peripheral neuropathy, with symptoms including numbness, tingling and weakness in the toes and fingers, sensory impairment to touch, pain, vibration and temperature, muscular weakness, blurred vision, coldness of extremities, loss of body weight and reflexes, and even paralysis. Frequent or prolonged contact may irritate the skin and cause a skin rash (dermatitis). None of the ingredients of this product comprising over 0.1% are classified as carcinogenic according to OSHA, National Toxicology Program (NTP), International Agency for Research on Cancer (IARC) or the American Conference of Governmental Industrial Hygienists (ACGIH). |
| Section III—Physical/Chemical Characteristics |
| Appearance | Liquid |  |  |
| Odor | Sweet ester odor | Odor threshold – not established |  |
| Chemical Type | Mixture |  |  |
| Physical State | Liquid |  |  |
| Boiling Point | 56 - 58°C (133 -136°F) |  |  |
| Specific Gravity | 0.922 |  |  |
| Percent Volatiles | 59.9 |  |  |
| Percent VOC’s | 135 g/L | Non-reactive |  |
| Vapor Density | 2.0 – 2.8 @25°C (77°F) |  |  |
| pH Factor | Not applicable |  |  |
| Solubility | Not soluble in water |  |  |
| Evaporation Rate | >1 (butyl acetate = 1) |  |  |
| Section IV—Fire and Explosion Hazard Data |
| Flash Point | -23°C (-9.4°F) |
| Flash Point Method | Closed cup |
| Auto-ignition Point | 225-455°C (437-851°F) |
| Flammability Class | Class 1B |
| Lower Explosive Limit | 1.2 |
| Upper Explosive Limit | 16 |
| Fire and Explosion Hazards | Extremely flammable liquid and vapor. |
| Extinguishing Media | Chemical foam, carbon dioxide (CO2), dry chemical, water spray or water fog. |
| Fire Fighting Instructions | Firefighters should wear self-contained breathing apparatus and full protective gear. |
| Section V—Reactivity Data |
| Stability | Stable |
| Hazardous Polymerization | Will not occur |
| Conditions To Avoid (Stability) | Avoid extreme temperatures. Keep away from ignition sources, heat and flames. |
| Incompatible Materials | Avoid contact with strong oxidizing agents, strong acids and strong bases. |
| Hazardous Decomposition Products | Toxic and irritating gases, vapor or fumes of carbon monoxide (CO), carbon dioxide (CO2) |
| Conditions To Avoid (Polymerization) | Product will not undergo polymerization. |
| Section VI—Toxicological Properties |
| Acute Studies | Chemical Name ORAL LD50 (rat) DERMAL LD50 (rabbit) INHALATION LC50 (rat) Methyl Acetate 6975 mg/kg > 5000 mg/kg > 16000 ppm (4-hr dose -rat) Chlorobenzotrifluoride >6800 mg/kg >2700 mg/kg 4479 ppm Light Naphtha >2000 mg/kg >2000 mg/kg >5000 ppm n-Hexane 25000 mg/kg No data 48000 ppm |
| Eye Effects | Causes severe irritation |
| Skin Effects | Causes irritation and possible allergic skin reaction (from defatting and drying of the skin) |
| Miscellaneous Toxicological Information | Toxicological testing has not been conducted for the product overall. Available toxicological data for individual ingredients are summarized below. |
| Ingredient(s) – Toxicological Data hexane LD50 (oral, 14-day old rat): 15840 mg/kg LC50 (male rat): 38500 ppm (4-hour exposure) methyl acetate LD50 (oral, rat): greater than 5000 mg/kg LD50 (skin, rabbit): greater than 5000 mg/kg LC50 (rat): 16000 ppm (4-hour exposure) |
| Section VII—Ecological Information |
| Excotoxicological Information This product contains components that will normally float on water. These components may be harmful to aquatic organisms and may cause long term adverse effects in the aquatic environment. Toxicity - Aquatic And Terrestrial Plants Contains components that are potentially toxic to freshwater and saltwater ecosystems. Environmental Fate Information Contains components with the potential to bio-accumulate. No specific information available. |
| Section VIII—First Aid Measures |
| Eye | In case of contact, hold eyelids apart and immediately flush eyes with plenty of water for at least 15 minutes. Get medical attention immediately if irritation develops and persists. |
| Skin | Remove contaminated clothing and shoes. Wash affected areas with soap and water. Get medical attention if symptoms occur. |
| Ingestion | Get medical attention immediately. DO NOT INDUCE VOMITING. Never give anything by mouth to an unconscious victim. |
| Inhalation | Remove the person from the contaminated area to fresh air. Ger medical attention immediately. |
| Note to Physician | Aspiration of liquid into the lungs during swallowing or vomiting can cause inflammation, serious lung damage and even death from chemical pneumonitis. |
| Section IX—Preventative Measures |
| Engineering Controls | Use with adequate general and local exhaust ventilation. When used outdoors, stay well away from building air intakes or close and seal the intakes to prevent product from entering building. |
| Personal Protective Equipment | Respiratory Protection: The level of respiratory protection needed should be based on the evaluation of chemical exposures by a health or safety professional. If required, use a NIOSH-approved air purifying respiratory with organic vapor cartridge and particulate filter or supplied air respirator. |
|  | Skin Protection: Use with chemical-protective gloves made of nitrile or neoprene to prevent skin contact. |
|  | Eye / Face Protection: Safety glasses with side shields recommended. |
| Occupational Exposure Limits for individual ingredients (if available) are listed below. Ingredient(s) – Exposure Limits HEPTANE ACGIH TLV-STEL 500 ppm ACGIH TLV-TWA 400 ppm OSHA PEL-TWA 500 ppm hexane ACGIH TLV-STEL 1000 ppm ACGIH TLV-TWA 50 ppm (Skin) ACGIH TLV-TWA 500 ppm OSHA PEL-TWA 500 ppm methyl acetate ACGIH TLV-STEL 250 ppm ACGIH TLV-TWA 200 ppm OSHA PEL-TWA 200 ppm Mineral Oil 5 mg/m3 |
| Section X—Handling and Storage |
| Handling and Storage Requirements | Keep away from ignition sources. Keep containers tightly closed. Store in a cool, dry, well-ventilated area. Do not handle or store near heat, sparks, flame, strong oxidents or strong acids. Use only with adequate ventilation. Ground all containers. |
| Accidental Release Measures | Wear adequate respiratory protection equipment. Ventilate area. Avoid open flames, sparks or other ignition sources. Contain any liquids and absorb spill with inert material (e.g. sand, vermiculite). Collect and dispose in accordance with applicable regulations. |
| Handling Precautions | SENSITIVE TO STATIC DISCHARGE: Likely to catch fire from near-by spark. Static charge may accumulate by flow or agitation. Grounding and bonding of containers is required. For professional or industrial use only. Follow label instructions. Keep out of the reach of children. Not for consumption. No smoking. Do not breathe vapors. Avoid contact with body. Turn off all pilot lights, flames, stoves, heaters, electric motors, welding equipment and other sources of ignition. Empty containers must not be washed and re-used for any purpose. Contact lens wearers must wear protective eye wear around chemical vapors and liquid. Wash hands thoroughly after handling. Flammable vapors may cause flash fire or ignite explosively. To prevent build-up of vapors, use adequate natural and/or mechanical ventilation (e.g. open all windows and doors to achieve cross ventilation). Containers may be hazardous when empty. Never use welding or cutting torch on or near container. Do not cut, drill, grind, or expose containers to heat, sparks, static electricity or other source of ignition. Explosion may occur causing injury or death. |
| Section XI—Disposal and Transportation |
| Disposal | Disposal In accordance with applicable federal, state and local government regulations. |
| Transport Information |
| Ground | UN1133, Adhesives, 3, PGII |
| IMDG | UN1133, Adhesives, 3, PGII |
| IATA | UN1133, Adhesives, 3, PGII |
| Section XII—Regulatory Information |
| SARA Hazard Classes | Acute Health Hazard Chronic Health Hazard Fire Hazard |
| Ingredient(s) - U.S. Regulatory Information hexane SARA Title III - Section 313 Form "R"/TRI Reportable Chemical State Regulations Warning! May contain trace amounts of chemicals known to the state of California to cause cancer and/or reproductive harm. Ingredient(s) - State Regulations HEPTANE New Jersey - Workplace Hazard New Jersey - Special Hazard Pennsylvania - Workplace Hazard Massachusetts - Hazardous Substance New York City - Hazardous Substance hexane New Jersey - Workplace Hazard New Jersey - Environmental Hazard New Jersey - Special Hazard Pennsylvania - Workplace Hazard Massachusetts - Hazardous Substance New York City - Hazardous Substance methyl acetate New Jersey - Workplace Hazard New Jersey - Special Hazard Pennsylvania - Workplace Hazard Massachusetts - Hazardous Substance New York City - Hazardous Substance |
| Canadian Regulatory Information | This product has been classified in accordance with the hazard criteria of the CPR and the MSDS contains all the information required by the CPR. WHMIS Classification: B2 - Flammable Liquid, D2B - Toxic. |
| Ingredient(s) - Canadian Regulatory Information hexane WHMIS - Ingredient Disclosure List |
| WHMIS – Canada (Pictograms) |
| NFPA |
| HMIS HEALTH 1 FLAMMABILITY 3 REACTIVITY 0 PERSONAL PROTECTION B |
| Disclaimer Although reasonable care has been taken in the preparation of this document, we extend no warranties and make no representations as to the accuracy or completeness of the information contained therein, and assume no responsibility regarding the suitability of this information for the user’s intended purposes or for the consequences of its use. Each individual should make a determination as to the suitability of the information for their particular purposes(s). |

The data and information is based on our knowledge to date and is intended to describe the product with regard to safety requirements. They are not to be interpreted as a specification of properties of the products described.

# Text boxes

0

1

3